## Slide 1: Seismic Noise and LIGO Why the biggest noise source isn’t the baddest
Conor Mow-Lowry

## Slide 2: Session 4
Seismic noise
  Physical origins
  Passive isolation
  Inertial sensors
Tutorial 2: Mechanics in the frequency domain.
  Calculate the response of a seismometer
  Build a noise budget with readout noise and thermal noise.

## Slide 3: Slido for questions
Add your questions or upvote those already posted and I’ll try to answer them.
Fully anonymous!
  Slido #921 8346
  https://app.sli.do/event/feM5JT34qMLuDUDwBXHDDH

## Slide 4: Tutorial material
Morning BND tutorial 1 – frequency noise (indico) Diagram on slides (on screen + indico)
(helpful) BND session 3 Maxwell_to_detection (indico) (optional) Session 3 notes - interferometer_techniques…
Afternoon BND tutorial 2 – sensor_response (indico) BND tutorial 2 notes – thermal noise (indico) Information on slides (on screen + indico)
(optional) BND tutorial 2 notes – pole_zero (indico)

## Slide 5: Just how big is ‘big’?
Here be dragons!

## Slide 6: Just how big is ‘big’?
Sam Cooper, PhD thesis, available at: https://core.ac.uk/download/pdf/286186961.pdf
Factor of 1010!

## Slide 7: Part 1: Seismic noise
Galaxy Quest

## Slide 8: Seismic noise: Surface waves
Microseisms: below 1 Hz
  Ocean waves interacting with seafloor
    Primary microseism (0.07 - 0.1 Hz)
    Secondary microseism (0.14 - 0.2 Hz)
Microtremors: above 1 Hz
  Human-made vibrations:
    Buildings
    Cars
    Machinery
  Environmental vibrations
www.geo.mtu.edu/UPSeis/
P-wave
Pressure wave
Primary wave
S-wave
Shear wave
Secondary wave
Particle motion
Particle motion
Love wave
Particle motion
Particle motion
Rayleigh wave

## Slide 9: Seismic noise model
Frequency [Hz]
Time [s] 1000 100 10 1 0.1
Microseisms
Microtremors

## Slide 10: Seismic noise model
Frequency [Hz]
Time [s] 1000 100 10 1 0.1
[Nature2007 V.445 Nr.7129 pp754-756]
doi:10.1038/nature05536
[Peterson 1993 OBSERVATIONS AND MODELING OF SEISMIC BACKGROUND NOISE]
Primary microseism
Secondary microseism
Earth‘s hum
Ground tilting
Human activity
Notes: The Earth responds to the Moon - Earth Tides
the surface of the solid earth moves only about 10 cm at most;
"normal modes" or "free oscillations"
In 1911 A.E.H. Love made the calculations and determined the period would be about an hour.
he first real proof came in 1961 by Bruce Bolt who clearly identified a 54 minute mode associated with the 1960 Chilean earthquake. He also saw much shorter period vibrations that represent harmonics or overtones of the fundamental long period mode.

## Slide 11: Seismic noise model
Frequency [Hz]
Time [s] 1000 100 10 1 0.1
Microseismic peak
Human activity
Earthquake
Measured in the
AEI basement

## Slide 12: Spectrogram of the ground velocity
2012-09-22
2012-10-03
Holiday
2012-10-07
Human activity
Earthquakes
Motors
Noisy
Quiet
Weekend
Measured in the
AEI basement
http://www.volcanodiscovery.com/earthquakes/archive/
Tue, 25 Sep 05:37 5.2 565 km 405 km S of the Fiji Islands

## Slide 13: Spectrogram of the ground velocity
2012-09-22
2012-10-03
2012-10-07
Human activity
Earthquakes
Motors
Noisy
Quiet
Weather conditions
Holiday
Weekend
Research platform FINO1
(Forschungsplattformen in Nord- und Ostsee)
45 km from Borkum
The meteorogical data are courtesy of the Bundesministerium für Umwelt, Naturschutz und Reaktorsicherheit and the Projektträger Jülich

## Slide 14: Part 2: Seismic isolation techniques
LOTR
Seismic noise: you shall not pass!

## Slide 15: Harmonic oscillator: pendulum
40
20
0
-20
-40
0.1 1 10
Frequency [Hz]
Transfer function [dB]
IN
OUT
Transfer function =
OUT
IN

## Slide 16: A mass on a spring
‘roll off’
1/f2

## Slide 17
Train suspension
…it’s just a mass on a spring

## Slide 18: Test Mass Isolation for Advanced LIGO
K2
K1
K1
K2
K3
K3
L1
L2
L3
L4
0.5M
M
M
0.5M
Prototype quad pendulum for Advanced LIGO
Test Mass
≈2 m
M = 40 kg
K4
K4
Credit: Brett Shapiro

## Slide 19: Quadruple Pendulum (Quad) Isolation
K2
K1
K1
K2
K3
K3
0.5M
M
M
0.5M
xg(t)
x4(t)
x4(s)/xg(s)
steep roll off!
K4
K4
Credit: Brett Shapiro
1/f8
GWs this way
-140db = 10-140/20
= 10-7
We need more!
Isolation at 10Hz

## Slide 20: Longest pendulum in the world
Tamarack mine shaft, Michigan (1901)
Payload: 22.7 kg (50 pounds)
Steel piano wire
  Length: ~1,3 km
  Ø 0.55 mm
  Wire streched by 4.5 m (15 feet)
Period: 70 s (14 mHz)
http://www.guinnessworldrecords.com/records-1/longest-pendulum/

## Slide 21: We need an extra step
We can’t go ‘taller’, very poor scaling
We can’t just add more stages, poor scaling and increased complexity
We add ‘pre-isolation’
Employ anti-springs to lower resonant frequencies
Use active feedback to damp and suppress motion

## Slide 22: We need an inertial sensor
“Something that measures the motion of an object relative to a free mass”
Special relativity says there is no preferred frame, and our free-mass (or proof-mass) has an undefined position and velocity.
Some examples:
  LISA Pathfinder
  LIGO
  Big-G experiments
  Seismometers
  Every (smart) phone!

## Slide 23: A mass on a spring
‘roll off’
1/f2

## Slide 24: The simplest concept
A mass on a spring (or a pendulum)

## Slide 25: Sensor response

## Slide 26: Plant inversion
Converting a relative position into an inertial output results in unbounded noise at low-frequency

## Slide 27: An ‘ideal’ inertial sensor
An ‘Ideal’ sensor has no readout noise (or actuation noise, or temperature coupling…), it is limited by force noise.
The lowest limit is suspension thermal noise: approximately white in force noise
More bending material  more loss  more noise.
But enough material is required to support a given mass

## Slide 28: Tutorial process
Calculate force noise from the spring
Apply force noise to the mass position, xm
Measure ∆x with a sensor
Apply sensor noise
Convert ∆x to xg, ‘plant inversion’
Plot sensing noise and thermal noise

## Slide 29: Tutorial Question!
[optional] Derive the response of a seismometer.
Plot the sensitivity transfer function [m/m] for an example seismometer with m=5kg, f0=1Hz, Q=40.
Plot the sensitivity to ground motion if you use a displacement readout with a noise floor of 10-13m/sqrt(Hz)
Compare with a velocity readout with 3x10-11m/s/sqrt(Hz).
Plot freq. vs disp. on log-log axes from 10mHz to 10Hz.
Add its suspension thermal noise to the plot. This is now a noise budget for your seismometer!